Archiver system design proposal & prototype

Provide design of storage and service layers that would be able to store 50000 double precision scalar signals with 14Hz frequency in a storage system.

# Recording Signals

The data in the storage system will be filled out by a number of “Archive Engines” running on different hosts. Each Archive Engine monitors the control system for a number of defined signals and uses a DataWriter service to write the values in the storage:

public interface DataWriter {
    public void addSample(EpochTime when, String signalName, double value);
}

EpochTime is abstract data-type with millisecond precision.

Please note that not all signals have 14Hz frequency, some might have 1Hz or lower frequency.

The mechanism of retrieval of the data samples from the control system should not be subject in the design. The design should cover the implementation of the DataWriter interface.
## Archive Engine Servers
The system should scale with addition of “Archive Engines”. Writing to the storage system is not necessary the bottle-neck in this case – data retrieval from the control system might be.

Processor:	Modern Quad-Core X86-64 processor – Intel Xeon E3
RAM:	16 GB
Storage:	2 RAID-0 2 TB disks
Network:	Gigabit Ethernet

## Data optimization
The data written in the storage system should be optimized for retrieval so that a number of users could be able to browse, plot and correlate years of data with sub-second precession.
Plotting should be arbitrarily scalable – a signal could be plotted on screen for a whole year but then user could zoom in to level detail of milliseconds.
Users might like to correlate signals with respect to time. This is also a possible optimization hint for both storage and retrieval purposes. The correlated signals might not necessary have been written with equal frequency (e.g. 14Hz and 1 Hz).
# Prototype
## Data retrieval service
Write and document a prototype data retrieval service that would facilitate implementation of a plotting client. It should support pre-fetching, data-reduction etc. so that the client could plot the signal in user friendly manner without lagging.
The data should reside in a storage system proposed by the design. The service should expose its functionality on a TCP/IP network.
For testing, the storage should be filled with data from some source such as audio samples or sin/cos generated values. It should contain year worth of data for at least 10 signals (at 14Hz sampling freq).
## Plotting client
Write and document a plotting client in Java that would use the Data Retrieval Service to plot a signal with arbitrary time frame. Panning/zooming should be done using combination of keys and mouse operations (movement/wheel).
For rendering on-screen, please use the Java SWT library.
Usage of open-source and copyleft third party libraries is allowed.

Here are some examples of an existing signal plotting solutions: